## Slide 1
Development of Temporal Land Cover Maps for Guam
25 September 2026
UOG Annex A Warehouse Building, Room 6
WERI GLE GHS Workshop 2026
Nicole Sulla Mathews, RA III
Dr. Yuming Wen, Professor of GIS
Water and Environmental Research Institute of the Western Pacific
University of Guam
Mangilao, GU 96923
USGS LANDSAT 8 (2020). USGS Earth Explorer https://earthexplorer.usgs.gov/

## Slide 2
Land Cover Mapping on Guam
Consistent, accurate land cover mapping is essential for assessing the potential impacts of rapid land transformation on the NGLA
Rapid transformation and urbanization introduce impervious surfaces that alter natural hydrology and potentially affects the pattern and rate of water recharge to NGLA and introduce contaminants
Project objective: development of a seasonally calibrated geospatial workflow that reconstructs 20+ years of land cover and land cover change to support groundwater sustainability
WERI GLE GHS Workshop 2026
Sulla Mathews 2
Image 1-3. Sentinel-2 Images of Camp Blaz, RGB:432, Copernicus (2026)
Image 4-6. Sentinel-2 Images of Marbo Solar Farm, RGB:432, Copernicus (2026)

## Slide 3
NOAA-provided LC maps are typically released every 5 years, missing rapid annual land cover transitions
C-CAP Limitations
Classification Class Gaps
Restrictions & Accuracy Uncertainty
WERI GLE GHS Workshop 2026
Current Knowledge Gaps
Existing datasets often lack Guam-specific classes necessary for basin research (active development/construction sites)
Limited local data regarding total accuracy of Guam LC maps (~80-85%)
C-CAP data is restricted from contributing/evaluating machine learning within 5 years of creation
It’s not intended for use in litigation
Sulla Mathews 3

## Slide 4
Data Selection & Reference Material
Landsat 7, 8, and 9 were selected for this project for their multi-decade historical record
Typically provides enough revisits annually to compile reasonably cloud-free mosaics for both wet and dry season
Reference material: Sentinel-2, Google Earth historical images, Pacific Islands Wildfire Data Explorer
WERI GLE GHS Workshop 2026
Image 7. Landsat Missions Timeline, USGS (2025)
Sulla Mathews 4
Image 8. Pacific Islands Wildfire Website, USDA, HWMO (2026)
Notes: Image link: https://www.usgs.gov/media/images/landsat-missions-timeline

## Slide 5
WERI GLE GHS Workshop 2026
Landsat is generally limited to 30m resolution, which can be challenging compared to 10m resolution of Sentinel-2
Spatial Resolution
Landsat 7 SLC Error
Data Sparsity
On May 31, 2003, SLC failed, which resulted in strips of missing data throughout all images taken since that time
Images prior to 2015 are more limited, necessitating the use of multi-year seasonal mosaics to achieve full island coverage
Data Limitations
Sulla Mathews 5
Notes: Image link: https://www.usgs.gov/media/images/landsat-missions-timeline

## Slide 6
Persistent Cloud Cover
Tropical environment makes obtaining a single-cloud free image significantly rare
WERI GLE GHS Workshop 2026
Mapping Challenges:
LANDSAT 8, Nov. 2024 (RGB: 4 3 2)
LANDSAT 7, March 2010 (RGB: 4 3 2)
LANDSAT 8, Nov. 2019 (RGB: 4 3 2)
*Faulty Scan Line Corrector from May 2003 – 2013
Sulla Mathews 6

## Slide 7
Spectral Variability & Seasonal Dynamics
Guam’s landscape shifts between dry season (Jan-June) of badlands & burn scar expansion and a wet season (July-December) of high vegetation vigor
WERI GLE GHS Workshop 2026
Mapping Challenges:
LANDSAT 8, Dry Season 2025
Images obtained from Jan-June 2025
LANDSAT 8, Wet Season 2025
Images obtained from July-Dec 2025
Sulla Mathews 7

## Slide 8
QA Pixel
SR Matching
Workflow:
Use the Remap function on the Quality Assurance (QA) layer to remap all pixels to NoData except land and water.
Use the Clip function on the Surface Reflectance layer to match the SR layer to the QA layer, effectively removing most clouds and shadows
Automated Cloud Masking
LANDSAT 8, 11 Nov. 2015
WERI GLE GHS Workshop 2026
Sulla Mathews 8

## Slide 9
Polygon Clipping
Workflow:
Polygons are digitized manually to outline missed cloud “halos”, shadows, thin clouds
Manual Refinement
Mosaic with manual refinement (Landsat 8, 2025 Dry Season)
Mosaic without manual refinement (Landsat 8, 2025 Dry Season)
WERI GLE GHS Workshop 2026
Sulla Mathews 9
Mosaic without manual refinement (Landsat 8, 2025 Dry Season)
Mosaic with manual refinement (Landsat 8, 2025 Dry Season)

## Slide 10
Supervised Classification
Base Training Set
Developed for stable classes (Forest, Water, Urban-Developed) to streamline process across years
Using Support Vector Machine (SVM)
Supplemental Training Set
Additional samples are added for classes that move or change such as burn scars or active construction sites (Urban-Undeveloped)
WERI GLE GHS Workshop 2026
Sulla Mathews 10

## Slide 11
Supervised Classification
Accuracy Assessment Preliminary Results
Dry Season
2025: 87% total accuracy, 0.85 Kappa
2020: 90% total accuracy, 0.89 Kappa
2015: 88% total accuracy, 0.86 Kappa
Wet Season
2025: 90.6% total accuracy, 0.89 Kappa
2020: 85.4% total accuracy, 0.83 Kappa
2012-2014: 81% total accuracy, 0.78 Kappa
WERI GLE GHS Workshop 2026
Sulla Mathews 11
Validation conducted through 50 random sampling points per class (7 classes) verified against high-resolution reference data

## Slide 12
Land Cover Maps
25 Land Cover Maps completed with overall accuracy >80% (as of Sept. 2026)
Limitations:
2000-2014: Multi-year mosaics (3-4 years)
WERI GLE GHS Workshop 2026
Sulla Mathews 12
Years/Season Completed | Not Enough Data
2025 (Dry + Wet) | 2008-2011 (Wet)
2024 (Dry + Wet) | 2004-2007 (Wet)
2023 (Dry + Wet) | 2000-2003 (Dry)
2022 (Dry + Wet) | 
2021 (Dry + Wet) | 
2020 (Dry + Wet) | 
2019 (Dry + Wet) | 
2018 (Dry + Wet) | 
2017 (Dry + Wet) | 
2015 (Dry + Wet) | 
2012-2014 (Dry + Wet) | 
2008-2011 (Dry) | 
2004-2007 (Dry) | 
2000-2003 (Dry) | 
2025 Dry Season (Jan-June)
2004-2007 Dry Season (Jan-June)

## Slide 13
Dry Season 2025
Supervised Classification
Dry Season Matrices
Columns: Ground Truth
Rows: Classified by SVM
Error of commission: overestimation – the classifier is seeing more of a class than there is
Error of omission: left out – the classifier misclassified a pixel for another class
WERI GLE GHS Workshop 2026
Sulla Mathews 13
Classifier correctly identified all badland random samples, but also falsely classified several other classes as badlands as well

## Slide 14
Dry Season 2000 - 2003
Supervised Classification
Dry Season Matrices
Columns: Ground Truth
Rows: Classified by SVM
Error of commission: overestimation – the classifier is seeing more of a class than there is
Error of omission: left out – the classifier misclassified a pixel for another class
WERI GLE GHS Workshop 2026
Sulla Mathews 14
Classifier under classified the target category – while highly accurate, it also missed other badlands found across the map

## Slide 15
Why does this mapping matter?
The Finegayan Basin comprises only 7% of the NGLA’s total surface area
Extensive buildup activities in the basin
From 18 wells operated by Guam Waterworks Authority (GWA) and the Naval Facilities Engineering Command (NAVFAC), the basin supplies ~15% of the aquifer’s total production
62.5% of wells in the basin show significant increase trends in chloride levels
By creating accurate annual maps, correlations between rapid urbanization and rising chloride levels can be quantified – providing a technical foundation for land-water resource management in Guam
GUAM ACM 2026
Image 4. Map of Study Area, Finegayan Basin
Sulla Mathews 15
Camp Blaz

## Slide 16
Next Steps
The Finegayan Basin comprises only 7% of the NGLA’s total surface area, supplies ~15% of total aquifer production
Recent study found 62.5% of wells in the Finegayan Basin show significant increase trends in chloride levels
By creating accurate annual maps, correlations between rapid urbanization and rising chloride levels can be quantified – providing a technical foundation for land-water resource management in Guam
WERI GLE GHS Workshop 2026
Image 4. Map of Study Area, Finegayan Basin
Sulla Mathews 16
Camp Blaz

## Slide 17
Water and Environmental Research Institute of the Western Pacific, University of Guam
https://weri.uog.edu | https://guamhydrologicsurvey.uog.edu
Nicole Sulla Mathews
Research Assistant III
+1-671-735-2685
mathewsn@triton.uog.edu
Thank you!
Slide Template provided by SlidesCarnival
USGS LANDSAT 8 (2020). USGS Earth Explorer https://earthexplorer.usgs.gov/
This research is partially funded by U.S. Geological Survey National Water Resource Institute 104(B) Program, and Guam Hydrological Survey.
Dr. Yuming Wen, GISP
Advisor, Professor of GIS
+1-671-735-2687
ywen@triton.uog.edu